## Slide 1
Eng. Laith Batarseh
Statics
Coplanar Forces

## Slide 2: Coplanar Forces
In this lecture
We will
  Define the concept of coplanar forces
  Study the cases of scalar notation
  Study the cases of Cartesian notation
  Learn how to sum forces

## Slide 3: Coplanar Forces
Coplanar forces
Coplanar forces are the forces that share the same plane.
These forces can be represented by their components on x and y axes which are called the rectangular components.
The components can be represented by scalar and Cartesian notations.
Scalar notation
Cartesian notation
Fx = F cos(θ)
y
x
Fy
Fx
F
θ
Fy= F sin(θ)
Fy
Fx
F
x
i
y
j
F = Fx i + Fy j

## Slide 4: Coplanar Forces
Scalar notation cases
y
x
Fy
Fx
F
θ
Fx = F cos(θ)
Fy= F sin(θ)
1
2
y
x
Fy
Fx
c
Fx /F= a/c
Fy /F= b/c
a
b
F

## Slide 5: Coplanar Forces
Cartesian notation cases
Fy
Fx
F
x
i
y
j
F2,y
F2
F2,x
F1,y
F1
F1,x
F4,x
F4
F4,y
x
y
F3,x
F3,y
F3
F 1= F1,x i + F1,y j
F 2 = -F2,x i + F2,y j
F 3= -F3,x i - F3,y j
F 4= F4,x i - F4,y j

## Slide 6: Coplanar Forces
Force summation
For both cases of notations, the magnitude of the resultant force is found by:
And the direction is found by:
FR,x =∑Fx
FR,y =∑Fy
FR,y
FR,x
FR
θ
+ve
+ve

## Slide 7: Coplanar Forces
Example [1]:
Question:
The hook shown in the figure is subjected to two tension forces F1 and F2. determine the magnitude and direction of the resultant force.
Solution:
Given: F1 =200∟200o and F1 =100∟-30o
Required: find the resultant force FR
Plan:
Find the resultant force by the scalar notation
Find the resultant force by the Cartesian notation
30o
20o
F1= 200 N
F2=100 N

## Slide 8: Coplanar Forces
Example [1]cont:
Solution:
Scalar notation
x – components: F1,x = - F1 cos(20) = - 188 N
F2,x = F2 cos(30) = 86.6 N
∑Fx = 86.6 – 188 = -101.4 N
y – components: F1,y = - F1 sin(20) = -68.4 N
F2,y = -F2 sin(30) = - 50 N
∑Fy = – 68.4 – 50 = – 118.4 N
Magnitude : FR = [(-104.4)2 + (-118.4)2] ½ = 157.9 N
Direction : θ = tan-1 |-118.4/-104.4| = 48.6o
200 N
30o
20o
100 N
-104.4N
-118.4 N
θ
y
x

## Slide 9: Coplanar Forces
Example [1]cont:
Solution:
Cartesian notation
Forces : F1 ={ - 188 i – 68.4 j} N
F2 = {86.6 i – 50 j} N
∑Fx = 86.6 – 188 = -101.4 i N
∑Fy = – 68.4 – 50 = – 118.4 j N
Magnitude : FR = [(-104.4)2 + (-118.4)2] ½ = 157.9 N
Direction : θ = tan-1 |-118.4/-104.4| = 48.6o
200 N
30o
20o
100 N
-104.4N
-118.4 N
θ

## Slide 10: Coplanar Forces
Example [2]:
Question:
There are 5 forces acting on the ring shown in the following figure. determine the magnitude and direction of the resultant force.
Solution:
Given: the magnitudes and directions for all forces
Required: find the resultant force F
Plan:
use the Cartesian notation to find the resultant force.
100 N
200 N
150 N
50N
60 N
45o
45o
30o
20o
x
y

## Slide 11: Coplanar Forces
Example [2]cont:
Solution:
Forces:
F1 = 200 cos(45) i + 200 sin(45) j
F1 ={ 141.42 i +141.42 j} N
F2 = 100 i + 0 j N
F3 = -150cos(45) i + 150sin(45) j ={ -106.06 i + 106.06 j} N
F4 = - 50 cos(30) i – 50 sin(30) j ={- 43.3 i - 25 j} N
F5 = 60 cos(20) i - 60 sin(20) j ={ 56.4 i - 20.52 j} N
Magnitude : Fx = 141.42+100 – 106.06 – 43.3 +56.4 = 148.46 N
Fy = 141.42 +0 +106.06 – 25 – 20.52 = 201.96 N
F = {148.46 i + 201.96 j} N
|F| = [ (148.46)2 + (201.96)2]½ = 250.66 N
Direction: θ = tan-1 |201.96/148.46| = 53.7o
100 N
200 N
150 N
50N
60 N
45o
45o
30o
20o
x
y
x
y
250.66 N
53.7o

## Slide 12: Coplanar Forces
P
Summary
Coplanar forces are the forces that share the same plane.
These forces can be represented by their components on x and y axes which are called the rectangular components.
The components can be represented by either scalar or Cartesian notations.
Resultant force can be found as:
FR,x =∑Fx
FR,y =∑Fy

## Slide 13: Coplanar Forces
P
End of lecture
See you in the next lecture
Don’t forget to answer the quiz