## Slide 1
Eng. Laith Batarseh
Statics
Cartesian Vectors
Part 2

## Slide 2: Cartesian Vectors
In this lecture
We will
  Learn new direction definition
  Learn how to add Cartesian Vectors
  Define the position vector

## Slide 3: Cartesian Vectors
Other direction definition
A = Ax i + Ay j + Az k
uA = cos(α) i + cos(β) j + cos(γ) k
A = |A| uA
= |A| cos(α) i + |A| cos(β) j + |A| cos(γ) k
= Ax i + Ay j + Az k

## Slide 4: Cartesian Vectors
Other direction definition cont
Az = A cos(ϕ)
A’ = A sin(ϕ)
Ax = A’ cos(θ) = A sin(ϕ) cos(θ)
Ay = A’ sin(θ) = A sin(ϕ) sin(θ)
θ
ϕ

## Slide 5: Cartesian Vectors
Cartesian Vectors Addition
A = Ax i + Ay j + Az k
B = Bx i + By j + Bz k
R = A+ B
= (Ax + Bx ) i + (Ay + By) j +(Az + Bz ) k
General rule:
FR = ∑F = ∑Fx i + ∑Fy j + ∑Fz k

## Slide 6: Cartesian Vectors
Example [1]:
Question: assume the following forces:
F1 = 5 i + 6j -4k
F2 = -3i +3j +3k
F3=7i-12j+2k
Find the resultant force F = F1 + F2 +F3 and represent it in both Cartesian and scalar notations
Solution:
Given: F1, F2 and F3
Required: find resultant force F and represent it in both Cartesian and scalar notation

## Slide 7: Cartesian Vectors
Example [1]:
Solution:
F = (5-3+7)i + (6+3-2)j +(-4+3+2)k = 9i +7j +10k (Cartesian notation)
Scalar notation:
Magnitude:
Unit vector u:

## Slide 8: Cartesian Vectors
Position vector
Assume: r = ai + bj + ck
At this point, r is called position vector.
Position vector is a vector locates a point in space with respect to other point.
in this case, vector r is a position vector relates point P to point O.

## Slide 9: Cartesian Vectors
Position vector
Assume vectors rA and rB are used to locate points A and B from the origin (ie. Point 0,0,0).
Define a position vector r to relate point A to point B.
rB = r + rA → r = rB – rA
r = (xB – xA)i + (yB – yA)j + (zB – zA)k

## Slide 10: Cartesian Vectors
Example [2]:
Question: if the robe shown in the figure extend from point A to point B. Find its length and direction measured from point A towards point B.
Solution:
Given: A(-5,3,2) and B(1.5,0,-2.5)
Required:
|r|
α, β and γ

## Slide 11: Cartesian Vectors
Example [2]cont:
Solution:
1. Position vector
A(-5,3,2) and B(1.5,0,-2.5)
r = (xB – xA)i + (yB – yA)j + (zB – zA)k
r = (1.5 – (-5))i + (0– 3)j + (-2.5– 2)k
r ={ 6.5i + – 3j + -4.5k} m
2. Robe length
3. Direction

## Slide 12: Cartesian Vectors
Summary
Position vector is a vector locates a point in space with respect to other point.
A = |A| cos(α) i + |A| cos(β) j + |A| cos(γ) k
FR = ∑F = ∑Fx i + ∑Fy j + ∑Fz k

## Slide 13: Cartesian Vectors
End of lecture
See you in the next lecture
Don’t forget to answer the quiz