## Slide 1
Eng. Laith Batarseh
Statics
Dot product

## Slide 2: Dot product
In this lecture
We will
  Learn the concept of dot product
  Find the angle between two intersecting vectors
  Finding vector components parallel and perpendicular to line

## Slide 3: Dot product
Dot product main concept
One of vector operations
Used to find the angle between two vectors share the same tail
Its result in scalar quantity
It is helpful when dealing with three-dimensions problems.

## Slide 4: Dot product
Notations
General formula: A.B = AB cos(θ)
Laws of operation:
Commutative Law: A.B = B.A
Multiplication by a scalar: a(A.B) = (aA).B = A.(aB)
Distributive Law: A.(B+D) = (A.B) + (A.D)
Cartesian formulation
A = Ax i + Ay j + Az k , B = Bx i + By j + Bz k → A.B = Ax Bx + Ay By + Az Bz
i.i = j.j = k.k = 1
i.j = j.i = i.k = k.i = j.k = k.j = 0
A
B
θ

## Slide 5: Dot product
Applications
Finding the angle between two intersecting vectors:
Finding vector components parallel and perpendicular to line
Aa = A cos(θ) = A.ua
Aa = Aa.ua
A┴= A -Aa
A
θ
Aa = Acos(θ) ua
A┴
ua
a
a

## Slide 6: Dot product
Example #1
Assume vector F has 200 N as shown in the figure. Find its projections onto the u and v axes.
Solution:
Fu = 200 cos(40o) = 153.2 N
Fv = 200 cos(20o) = 187.9 N
u
v
F =200N
20o
40o

## Slide 7: Dot product
Example #2
Assume the force vectors F1 and F2 have a common start point
F1 = 5 i + 6j -4k
F2 = -3i +3j +3k
Find the angle between these forces

## Slide 8: Dot product
Example #2
Solution:
But
So

## Slide 9: Dot product
P
Summary
Dot product is one of vector operations and results in scalar quantity
it is used to:
Find the angle between two intersecting vectors:
Find vector components parallel and perpendicular to line

## Slide 10: Dot product
P
End of lecture
See you in the next lecture
Don’t forget to answer the quiz