## Slide 1
Chapter Ten
Laith Batarseh
Statics
10. Work principle
By
Home
Next
Previous
End

## Slide 2
Statics
Work principle
Work
Work is defined as the effect of force on a body presented on translational motion in the same direction of the force
F
D
Work (W) = F.D

## Slide 3
Statics
Work principle
Work
In general, if a force F acts on body and undergoes differential displacement equal dr has an angle from the line of action equal θ as shown in the figure
F
θ
dr

## Slide 4
Statics
Work principle
Work
Now, this force produce a differential work element (dU) by its component that acts in the same direction of displacement (i.e. Fcos(θ))
The work done by this component is calculated as:
dU = F.dr cos(θ)
F
θ
dr
F
θ
dr
Fcos(θ)

## Slide 5
Statics
Work principle
Work properties
Work properties
Scalar
In Joule (J)

## Slide 6
Statics
Work principle
Work of couple moment
A
B
A’
B’
drA
drA
drB
B’’
dr'
dθ
F
-F
drA is translational motion
dθ is rotational motion about point A
dU=Fdr’’
dr’’=r .dθ
M=F.r
dU=M.dθ

## Slide 7
Statics
Work principle
Virtual work
Virtual work is the work done by a force that has a virtual displacement:
δU = F cos(θ).δr
Or the work done by a moment having a virtual rotation:
δU = M .δθ

## Slide 8
Statics
Work principle
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz