## Slide 1
Chapter Ten
Laith Batarseh
Statics
Work principle
By
Home
Next
Previous
End

## Slide 2
Statics
Work principle
Example 11.3
If the box in Figure has a mass of 10 kg, determine the couple moment M needed to maintain equilibrium when θ=60o. Neglect the mass of the members.
Engineering mechanics: static, 12th edition in SI units, R.C. Hibbeler, 2010

## Slide 3
Statics
Work principle
Example 11.2
Solution
Engineering mechanics: static, 12th edition in SI units, R.C. Hibbeler, 2010
F.B.D

## Slide 4
Statics
Work principle
Example 11.2
Solution
Virtual Displacements.
yE = 0.45 sin(θ)+ b
Differential elements
δyE = 0.45 cos(θ) δ(θ)
Virtual work equation
dU = 0 → M δ(θ)– [10(9.81)] δyE = 0

## Slide 5
Statics
Work principle
Example 11.2
Solution
Mδ(θ) - 10(9.81) (0.45 cos(θ) δ(θ)) = 0
→ {M- 44.145 cos(θ)} δ(θ)=0
Because δ(θ) ≠ 0
M- 44.145 cos(θ)=0
θ = 60o
M= 44.145 cos(60)=22.1 N.m

## Slide 6
Statics
Work principle
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz