## Slide 1: Statics
Eng. Laith Batarseh
Coplanar
Forces

## Slide 2: Coplanar Forces
In this lecture
We will
  Use equilibrium conditions to find unknown forces in given configuration

## Slide 3: Coplanar Forces
Equilibrium conditions:
∑F = 0
∑Fx i + ∑Fy j = 0
∑Fx = 0
∑Fy = 0

## Slide 4: Coplanar Forces
Procedures for analysis
FBD
Coordinate system (x and y axes)
Force Labeling (magnitude and direction)
Assuming the sense of the unknown forces
Equilibrium equations
Positive and negative assigning
Define the direction of the solution
∑ Fx = 0 and ∑ Fy = 0

## Slide 5: Coplanar Forces
Example[1]
Question:
Find the mass of the 2nd box needed to make this config-uration in equilibrium state.
Given: 1. one load
2. the directions of tension forces in cables
3. equilibrium condition
Solution: decompose the forces to its components and apply the equilibrium equations at points A and B

## Slide 6: Coplanar Forces
Example[1] cont
Fy = 0
T1sin(30)-T2sin(10)-981 = 0 --- Eq.2
Substitute Eq.1 in Eq.2 and solve for T1
T1 = 3031N
Back to Eq.1→ T2 = 2665 N
∑Fx = 0
-T1cos(30)+T2cos(10) = 0

## Slide 7: Coplanar Forces
Example[1] cont
Fy = 0
T3sin(60)+T2sin(10)-F= 0 --- Eq.2
Substitute the obtained values for T2 and T3 to find F
F=5009N → 511 kg
∑Fx = 0
-T2cos(10)+T3cos(60) = 0
T3 =5250N

## Slide 8: Coplanar Forces
Example[2]
6m
8m
3m
4m
50 kg
A
B
C
Question: find the tensile forces generated in members AB and AC when the 50 kg load is applied knowing that this configuration is in equilibrium state.
Given:
The load
Equilibrium state
Solution:
1.Drawing FBD
2. Apply equilibrium equations

## Slide 9: Coplanar Forces
Example[2]cont
Solve Eqs 1 and 2 to find FAC and FAB

## Slide 10: Coplanar Forces
Example[3]
Question: determine the stretch in springs AB and AC when the 50 kg load is applied knowing that this configuration is in equilibrium state.
Given:
The load
Equilibrium state
Solution:
1.Drawing FBD
2. Apply equilibrium equations
6m
3m
4m
50 kg
A
B
C
8m
KAC = 300N/m
KAB = 500 N/m

## Slide 11: Coplanar Forces
Example[3]cont
Solve Eqs 1 and 2 to find FAC and FAB

## Slide 12: Coplanar Forces
Example[4]
Question: The box held the given configuration in equilibrium and the unstretched length of spring AC is 8m. Determine the mass of the wooden box.
Given:
Spring AC unstreched length
Equilibrium state
Solution:
1.Drawing FBD
2. Find the force in spring AC
3. Apply equilibrium equations
6m
3m
4m
M=??
A
B
C
8m
KAC = 300N/m
KAB = 500 N/m

## Slide 13: Coplanar Forces
Example[4]cont
FAC = kAC xAC = 300*(10-8) = 600N
M = 1000/9.81 = 102 kg

## Slide 14: Coplanar Forces
Summary
∑F = 0
∑Fx i + ∑Fy j = 0
∑Fx = 0
∑Fy = 0

## Slide 15: Coplanar Forces
End of lecture
See you in the next lecture
Don’t forget to answer the quiz