## Slide 1
Chapter Three
Laith Batarseh
Statics
1. Moment Scalar
By
Home
Next
Previous
End

## Slide 2
Statics
Moment Scalar
In this lecture
  Define the concept of moment
Home
Next
Previous
End
  Learn how to sum moments

## Slide 3
Statics
Moment Scalar
Definition
  Moment is defined as the tendency of a body lies under force to rotate about a point not on the line of the action of that force (i.e. there is a distance between the force and the rotation point )
Home
Next
Previous
End
  The acting force
  Moment arm
Description
Moment depends on two variables:
  Moment is a vector quantity

## Slide 4
Statics
Moment Scalar
Home
Next
Previous
End
Description
Force
Arm
Tendency to rotate

## Slide 5
Statics
Moment Scalar
Home
Next
Previous
End
Tendency for rotation

## Slide 6
Statics
Moment Scalar
Home
Next
Previous
End
Magnitude
F
D
Moment magnitude (M) = F.D

## Slide 7
Statics
Moment Scalar
Home
Next
Previous
End
Direction

## Slide 8
Statics
Moment Scalar
Solving procedures
Home
Next
Previous
End
1. Define the magnitudes of force (F) and arm (D)
2. Assume the positive direction (eg. Counter clock wise)
3. Find the magnitude of moment (M) as F.D
4. Give the moment the correct sign according to the tendency for rotation

## Slide 9
Statics
Moment Scalar
Home
Next
Previous
End
Example [1]
  Find the moment caused by the following forces about point O
100 N
0.5m
2m
(b)
O
100 N
0.5m
2m
(a)
O

## Slide 10
Statics
Moment Scalar
Home
Next
Previous
End
Example [1]
Assume the CCW direction is the positive direction.
100 N
0.5m
2m
(b)
O
100 N
0.5m
2m
(a)
O
Branch (a)
Mo = F.d = -(100N)(0.5m)
Mo=-50 N.m=50N.m CW
Branch (b)
Mo=F.d = (100N)(2m)
Mo=200 N.m CCW
+
+

## Slide 11
Statics
Moment Scalar
Home
Next
Previous
End
Moment resultant
F1
F2
F3
d1
d2
d3
M1
O
M2
M3
Mo = ∑Mo = M1 + M2 – M3 = F1d1+F2d2 – F3d3
+

## Slide 12
Statics
Moment Scalar
Home
Next
Previous
End
Example [2]
  Find the moment caused by the following forces about point O
2m
3m
5m
1m
30o
100 N
50 N
60 N
75 N
O

## Slide 13
Statics
Moment Scalar
Home
Next
Previous
End
Example [2]
2m
3m
5m
1m
30o
100 N
50 N
60 N
75 N
O
+

## Slide 14
Statics
Moment Scalar
Home
Next
Previous
End
Exercise
  Find the moment caused by the following forces about point O
100 N
300 N
5m
2m
45o
30o
O
0.3m

## Slide 15
Statics
Moment Scalar
Home
Next
Previous
End
Exercise
+
100 N
300 N
5m
2m
O
0.3m
300 sin (45)N
300 cos (45)N
100sin (30)N
100cos (30)N

## Slide 16
Statics
Moment Scalar
Home
Next
Previous
End
Summary
Moment is the tendency to rotate produced by a force
Moment is vector quantity
The scalar magnitude of the moment equal to : F.d
The direction of the moment will be in a direction perpendicular to the plane which contains the vectors of the F and d

## Slide 17
Statics
Moment Scalar
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz