## Slide 1
Chapter Three
Laith Batarseh
Statics
2. Moment vector
By
Home
Next
Previous
End

## Slide 2
Statics
Moment vector
In this lecture
  Find the moment using cross product
Home
Next
Previous
End

## Slide 3
Statics
Moment vector
Cross product
Home
Next
Previous
End
Cross product is a mathematical operation can be done on vectors
Cross product for one time is done for two vectors
The cross product of two vectors is a vector perpendicular to the plane of A and B
The notation of vector A cross vector B is: C = AxB where C is the resultant vector from the cross product
the vector C can be represented as : C =CUc where Uc is a unit vector in a direction perpendicular to the plane that contains both A and B.
The value of the scalar quantity C is given as : C=A.B.sin(ϕ)
where ϕ is the angle between A and B.
The cross product is controlled by the right-hand rule

## Slide 4
Statics
Moment vector
Home
Next
Previous
End
Graphical representation
ϕ
Uc

## Slide 5
Statics
Moment vector
Home
Next
Previous
End
Laws of operation
Commutative Law is not valid: AxB ≠ BxA. AxB = -BxA
Multiple by scalar: s(AXB)= (sA)xB = Ax(sB)= (AXB)s
Addition: Ax(B+D) = (AxB) + (AxD)

## Slide 6
Statics
Moment vector
Home
Next
Previous
End
Cartesian vector formulation
i=jxk
j=kxi
K=ixj
y
x
z

## Slide 7
Statics
Moment vector
Home
Next
Previous
End
Cartesian vector formulation
A = Ax i + Ay j + Az k
B = Bx i + By j + Bz k
AxB=(Ay Bz -Az By )i-(Ax Bz - Az Bx )j + (Ax By - Ay Bx )k

## Slide 8
Statics
Moment vector
Home
Next
Previous
End
Moment – vector formulation
F
r
θ
d
M
O
x
y
Magnitude: Mo = rFsin(θ) = Fd
Direction: perpendicular to x-y plane (z-direction)
Matrix notation:
Resultant moment:MRo = ∑(rxF)
Best for three dimensional problems
Mo = rxF

## Slide 9
Statics
Moment vector
Home
Next
Previous
End
Example [1]
  Find the moment caused by the following forces about point O
F = [5i + 10j + 6k]N
z
x
y
3m
2m
1m
O

## Slide 10
Statics
Moment vector
Home
Next
Previous
End
Example [1]
1. Formulate the position vector (r) : r = 3i+2j+1k
2. Find the moment vector (Mo) by matrix notation
F = [5i + 10j + 6k]N
r = 3i+2j+1k

## Slide 11
Statics
Moment vector
Home
Next
Previous
End
Example [2]
  Find the moment caused by the following forces about point O
x
y
z
O
F = [-5i + 5j -5k]N

## Slide 12
Statics
Moment vector
Home
Next
Previous
End
Example [2]
1. Formulate the position vector (r) : r= 15i + 10j +6k
2. Find the moment vector (Mo) by matrix notation

## Slide 13
Statics
Moment vector
Home
Next
Previous
End
Summary
Moment is a vector can be found by cross product and matrix notation
Matrix notation:

## Slide 14
Statics
Moment vector
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz