## Slide 1
Chapter Three
Laith Batarseh
Statics
3. Principle Of Moments
By
Home
Next
Previous
End

## Slide 2
Statics
Principle Of Moments
In this lecture
  Learn the principle moment
Home
Next
Previous
End

## Slide 3
Statics
Principle Of Moments
Principle of Moments
Home
Next
Previous
End
some times called Vrigonon’s theorem (Vrigonon is French mathematician 1654-1722).
State that the moment of a force about a point equals the summation of the moments created by the force components
In two dimensional problems: the magnitude is found as M = F.d and the direction is found by the right hand rule
In three dimensional problems: the moment vector is found by M =rxf and the direction is determined by the vector notation (ie. i,j and k directions)

## Slide 4
Statics
Principle Of Moments
Home
Next
Previous
End
Example [1]
  Find the moment caused by the following forces about point O

## Slide 5
Statics
Principle Of Moments
Example [1]
Mo,1 = 100 sin(30) (10) = 500 N.m
Home
Next
Previous
End
+
Mo,2 =- 100 cos(30) (5) =- 433N.m
+
M = Mo,1+Mo,2=500-433=67N CCW

## Slide 6
Statics
Principle Of Moments
Home
Next
Previous
End
Example [2]
The following is a gate. In which direction this gate will rotate?
100N
120N
1.2 m
0.3 m
60o
40o

## Slide 7
Statics
Principle Of Moments
Home
Next
Previous
End
Example [2]
1. Force analysis
100 cos(40)
1.2 m
0.3 m
100 sin(40)
120 cos(60)
120 sin(60)
2. Moment calculations
∑ M = (100 cos(40))(1.5) –( 120 cos(60))(1.2) =43 N.m CCW
+

## Slide 8
Statics
Principle Of Moments
Home
Next
Previous
End
Example [3]
Find the moment caused by the following forces about point O

## Slide 9
Statics
Principle Of Moments
Home
Next
Previous
End
Example [2]
r1= 15i + 10j +6k F1 = [5j]N
r2= 15i + 10j -6k F2 = [-5j]N

## Slide 10
Statics
Principle Of Moments
Home
Next
Previous
End
Summary
In two dimensional problems: the magnitude is found as M = F.d and the direction is found by the right hand rule
In three dimensional problems: the moment vector is found by M =rxf and the direction is determined by the vector notation

## Slide 11
Statics
Principle Of Moments
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz