## Slide 1
Chapter Three
Laith Batarseh
Statics
4. Moment of force about axis
By
Home
Next
Previous
End

## Slide 2
Statics
Moment of force about axis
In this lecture
  Learn how to find the moment produced by a force about certain axis
Home
Next
Previous
End

## Slide 3
Statics
Moment of force about axis
Home
Next
Previous
End
In many real cases, the force tendency to rotate is about a specified axis.
Example :
Moment components:
  Mo,1 = (100)(10) (about y-axis)
  Mo,2 = (100)(15) (about x-axis)
  Mo,3 =0 (about z-axis)

## Slide 4
Statics
Moment of force about axis
Home
Next
Previous
End
Magnitude
Scalar analysis: M = F.d
Vector analysis:
Where: ua is a unit vector defining the direction of a-axis and given as
ua = ua,x i + ua,y j + ua,z k
To find the moment vector (Ma): Ma. ua

## Slide 5
Statics
Moment of force about axis
Example [1]
Mo,1 = 100 sin(30) (10) = 500 N.m
Home
Next
Previous
End
+
Mo,2 =- 100 cos(30) (5) =- 433N.m
+
M = Mo,1+Mo,2=500-433=67N CCW

## Slide 6
Statics
Moment of force about axis
Home
Next
Previous
End
Example [1]
Find the resultant moment produced by the following forces about axes: x, y and z.
F1=100N
F2=200N
F3=300N
x
y
z
O
0.5 m
0.5 m
0.5 m
0.25 m

## Slide 7
Statics
Moment of force about axis
Home
Next
Previous
End
Example [1]
F1=100N
F2=200N
F3=300N
x
y
z
O
0.5 m
0.5 m
0.5 m
0.25 m

## Slide 8
Statics
Moment of force about axis
Home
Next
Previous
End
Example [2]
Determine the magnitude of the moments of the force F about the x, y, and z axes. Solve the problem
  using a Cartesian vector approach
  using a scalar approach.

## Slide 9
Statics
Moment of force about axis
Home
Next
Previous
End
Example [2]
using a Cartesian vector approach
rAB = {5i + 4j -3k} m
For the axes: x, y and z the unit vectors are i, j and k respectively.
Mx = i . (rAB x F)
My = j . (rAB x F)
Mz = k . (rAB x F)

## Slide 10
Statics
Moment of force about axis
Home
Next
Previous
End
Example [2]
using a scalar approach
Mx = ∑Mx = 10(3) – 4(4) = 14 N.m
My = ∑My = -5(3) + 4(5) = 5 N.m
Mz = ∑Mz = -5(4) + 10(5) = 30N.m

## Slide 11
Statics
Moment of force about axis
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz