## Slide 1
Chapter Three
Laith Batarseh
Statics
5.2. Moment of couple
By
Home
Next
Previous
End

## Slide 2
Statics
Moment of couple
Home
Next
Previous
End
in many of life applications, an equivalent couple is required to solve some technical problems such as space and size.
Equivalent couples are the couples that have the same magnitude and same direction
As you can see, the relation between the forces and the arm distances in equivalent coupels is reverse (for example, as we reduce the moment arm, the required force for equivalent couple increases)
Equivalent couples
F1
-F1
d1
d2
F2
-F2
=
F1.d1 = F2.d2

## Slide 3
Statics
Moment of couple
Home
Next
Previous
End
Resultant couple is the vectorial summation of the couples act on the body as you can see.
In simple situation as shown in the figure, the parallelogram is used to sum the moments and in more complicated cases or three dimensional problems, the Cartesian notation is used.
Resultant couple
M1
M2
M1
M2
MR

## Slide 4
Statics
Moment of couple
Example [1]
Home
Next
Previous
End
The member shown in the figure is subjected to three coupling forces : 150, 200 and 100 N. the moment arms are shown.
If All dimensions in m, find the resultant couple moment produced by the following forces.
150 N
150 N
100N
100N
200N
200N

## Slide 5
Solution:
First, the Moment direction:
Second, the calculate the coupled moments
M1 = -(200)(13) = -2600 N.m
M2 = -(150)(7) = -1050 N.m
M3 = - (100)(8) = -800 N.m
Finally, calculate the moment sum (resultant)
MT = -2600-1050 -800=-4450 N.m
MT = 4450 N.m (clockwise)
Statics
Moment of couple
Example [1]
Home
Next
Previous
End
+

## Slide 6
Statics
Moment of couple
Example [2]
Home
Next
Previous
End
The member shown in the figure is subjected to two coupling forces : 200 and 100 N. the moment arms are shown.
Find the resultant couple moment produced by the following forces.
3m
3m
6m
0.6m
45o
100 N
100 N
200 N
45o
200 N

## Slide 7
Solution:
First, the Moment direction:
Second, the calculate the coupled moments
M1 = -(100)(0.6) = -60 N.m
M2,x = (200 cos(45))(0.6) = 85 N.m
M2,y = -(200 sin(45))(3) = -424 N.m
Finally, calculate the moment sum (resultant)
MT = -60+85-242=-399 N.m
MT =399 N.m (clockwise)
Statics
Moment of couple
Example [2]
Home
Next
Previous
End
+

## Slide 8
Statics
Moment of couple
Home
Next
Previous
End
For three dimensional problems, it is better to use the Cartesian notation (I, j and k) to represent the monuments.
The moment in a direction not one of the principle axes (x, y or z) can be represented as: M = Mu. Where u is a unit vector in the direction of the moment M.
The resultant moment can be found finally by vector addition for the moments vectors
3-D problems

## Slide 9
Statics
Moment of couple
Home
Next
Previous
End
3-D problems
M1
M2
x
z
y
θ
Example:
The figure show an object subjected to two moments: M1 and M2. as you can see M2 has an angle θ from the y-axis. The moment M1 can be represented as: M1= M1i.
While the moment
M2 can be represented as:
M2 = M2 (0i + cos(θ) j + sin(θ) k)

## Slide 10
Statics
Moment of couple
Home
Next
Previous
End
Summary
Equivalent couples are the couples that have the same magnitude and same direction
Resultant couple is the summation of the couples act on the body
In three dimensional problems, Cartesian notation is more convenient

## Slide 11
Statics
Moment of couple
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz