## Slide 1
Chapter Three
Laith Batarseh
Statics
6.1. Simplification of a force and couple system
By
Home
Next
Previous
End

## Slide 2
Statics
Simplification of a force and couple system
Home
Next
Previous
End
In many of situation where there a group of forces and moments acting on an object, it is seem more convenient to reduce the large number of forces and moments to one force and one moment.
Physical meaning: replacing a system of forces and moments by a system of one force and one moment.
Condition: the external effects produced by the forces and moments on the body for the original system are the same of the single force and moment in the new simplified system

## Slide 3
Statics
Simplification of a force and couple system
Home
Next
Previous
End
Simplification conditions
B
A
B
F
F
-F
F
Note: the acting force can be transport from one position to another on its line of action (i.e. force vector)
A
B
A
B
F
M = F.d
F
Note: the force acts on a member can be transport from one position to another on a line perpendicular force vector by adding the moment generated by the original force (i.e. M=F.d)

## Slide 4
Statics
Simplification of a force and couple system
Home
Next
Previous
End
Simplification conditions
F1
O
F2
r1
r2
M
Assume an object as shown in Fig.a is subjected to two forces ( F1 and F2) and one moment M. The forces F1 and F2 has a position vectors r1 and r2 respectively from the rotation point O to the line of action for each force.
Fig.a

## Slide 5
Statics
Simplification of a force and couple system
Home
Next
Previous
End
Simplification conditions
To convert the previous system into one force-moment system we must:
first move each force to the point of rotation O. this step include adding the moments produced by both forces (M1 and M2 respectively )at the rotation point as shown in the Fig.b.
Fig.b
O
F2
M
M1 = r1 x F1
M2 = r2 x F2
F1

## Slide 6
Statics
Simplification of a force and couple system
Home
Next
Previous
End
Simplification conditions
Then all forces and moments are summed using the following formulas:
FR = ∑F
MR,O = ∑MO + ∑M
Fig.c
O
FR
MR,o

## Slide 7
Statics
Simplification of a force and couple system
Example [1]
Home
Next
Previous
End
Figure below shows a plate a group of forces (100, 150, 200 and 300 N)
If All dimensions in m, Simplify the following force system to single force and moment system about point O

## Slide 8
Solution:
First, calculate the resultant force FR
∑Fx = 300 – 100 = 200 N
∑Fy = 200 + 150 = 350 N
Second, calculate the resultant moment MR
MR =-(200)(13) – (300)(4) –(150)(5) – (100)(4) = 4950 N.m
Finally, represent the new force and moment on the original system as shown.
Statics
Simplification of a force and couple system
Example [1]
Home
Next
Previous
End

## Slide 9
Statics
Simplification of a force and couple system
Example [2]: couple resultant
Home
Next
Previous
End
The system shown in the figure is subjected to two coupling forces : 200 and 100 N. the moment arms are as shown.
Simplify the following force system to single force and moment system about point O
3m
3m
6m
0.6m
45o
100 N
100 N
200 N
45o
200 N
399 N.m

## Slide 10
Solution:
First, the Moment direction:
Second, calculate the coupled moments
M1 = -(100)(0.6) = -60 N.m
M2,x = (200 cos(45))(0.6) = 85 N.m
M2,y = -(200 sin(45))(3) = -424 N.m
Finally, calculate the moment sum (resultant)
MT = -60+85-242=-399 N.m
MT =399 N.m (clockwise)
Note that the resultant force (FR ) = 0 which is true for all the coupled forces systems
Statics
Simplification of a force and couple system
Example [2]
Home
Next
Previous
End
+

## Slide 11
Statics
Simplification of a force and couple system
Example [3]
Home
Next
Previous
End
The three forces act on the pipe assembly. If F1 = 50 N and F2 = 80 N, replace this force system by an equivalent resultant force and couple moment acting at O. Express the results in Cartesian vector form..

## Slide 12
Solution:
First, calculate the resultant force FR
Finally, calculate the resultant moment MR using cross product
Statics
Simplification of a force and couple system
Example [3]
Home
Next
Previous
End

## Slide 13
Statics
Simplification of a force and couple system
Home
Next
Previous
End
Summary
To replace a system of forces and moments to single force and moment system, the external effects produced by the forces and moments on the body for the original system are the same of the single force and moment in the new simplified system.
The magnitude and the direction of force remain the same as it moves along its line of action
If the force produce a moment about a certain point, this moment must be compensated about that point.

## Slide 14
Statics
Simplification of a force and couple system
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz