## Slide 1
Chapter Three
Laith Batarseh
Statics
6.2. Simplification of a force and couple system
By
Home
Next
Previous
End

## Slide 2
Statics
Simplification of a force and couple system
Home
Next
Previous
End
Concurrent forces: forces that’s lines of action intersect at a common point
Concurrent forces are simply summed to find FR and as seen the moment is zero due to the passing of forces lines of action through the rotation point
Special cases:
F1
F2
F4
F3
O
FR
O
=

## Slide 3
Statics
Simplification of a force and couple system
Home
Next
Previous
End
Coplanar forces: forces share the same plane
Coplanar forces produce moments about the point of rotation and are summed to find FR . All the moments produced by the acting forces are summed to find the equivalent moment M.
Special cases:
F1
F2
F4
F3
O
FR
O
M
=

## Slide 4
Statics
Simplification of a force and couple system
Home
Next
Previous
End
Parallel forces system:
F2
F1
F3
F4
O
z
FR = ∑F
O
z
MR,O
b
a
FR = ∑F
O
z
b
a
d
A reverse process can be done to transform the single force – moment system into a single force with moment arm from the rotation point

## Slide 5
Statics
Simplification of a force and couple system
Home
Next
Previous
End
Establish the coordinate system (x, y and z axes). It is preferred to put the origin of this system at the rotation point.
Force summation
find the resultant force by summing the acting forces. You may resolve the forces to their rectangular components.
Moment summation
The resultant moment is the summation of the moments acting on the body and the moments produced by the acting forces.
Analysis procedures

## Slide 6
Statics
Simplification of a force and couple system
Home
Next
Previous
End
In three dimensional systems, we can find an equivalent force and moment. However, in general cases the moments and force are not perpendicular to each other. Because of that, it become impossible to reduce the system to single force with moment arm from the rotation point.
Special cases:

## Slide 7
Statics
Simplification of a force and couple system
Example [1]
Home
Next
Previous
End
Replace the following forces-moment system to a single force system.
5m
10 kN
7 kN
30o
2m
8m

## Slide 8
Solution:
First, calculate the resultant force F
∑Fx = 10 + 7cos(30) = 16.06kN
∑Fy = - 7 sin(30) = 3.5 kN
Second, calculate the resultant moment MR
MR =-(7sin30)(5) -(7cos30)(8)-(10)(8-2) = 126 kN.m
Finally, you can represent the new force and moment on the original system.
Xo= MR/FR = 126/16.43 = 7.67 m from the base point
Statics
Simplification of a force and couple system
Example [1]
Home
Next
Previous
End

## Slide 9
Statics
Simplification of a force and couple system
Example [2]
Home
Next
Previous
End
Replace the following forces-moment system to a single force system.
3m
3m
3m
x
z
y
200N
300 N
600 N
4m

## Slide 10
Solution:
First, calculate the resultant force F
FR = 300 + 600 – 200 = (700k) N
Second, calculate the resultant moment Mx and My
Mx =(300)(0) – (200)(3) + (600)(6) = 3000 N.m = FRy → y = 4.29m
My =-(300)(3) + (200)(0) - (600)(4) = 3300N.m = FRx→ x = 4.71m
Statics
Simplification of a force and couple system
Example [2]
Home
Next
Previous
End

## Slide 11
Solution:
Finally, you can represent the new force on the original system.
Statics
Simplification of a force and couple system
Example [2]
Home
Next
Previous
End
x
z
y
700 N
4.29m
4.72 m

## Slide 12
Statics
Simplification of a force and couple system
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz