## Slide 1
Chapter Three
Laith Batarseh
Statics
7.1 distributed loads
By

## Slide 2
Statics
Distributed Loads
Uniform loading along a single axis
x
w
L
w = w(x)
x
w
L
dF = dA
x
dx
w = w(x)
Distributed force is a force acting on a line or surface of the rigid body. The value of this force (w) is represented by a function in terms of dimensions. For example: w(x).
The force function could be linear or none linear
We can represent the distributed force by a single. To do that we first take an infinitesimal segment of the distributed force (dF) which equal the infinitesimal segment of the area under the force function as you can see on the screen

## Slide 3
Statics
Distributed Loads
Magnitude of resultant force
x
FR
w
w = w(x)
Let us first assume a distributed force w(x) acting on the member as shown in the fig.
Now, assume there is an equivalent force called FR for the distrusted force w(x) and it is located at a distance equal x’
The magnitude of FR can obtained by integrating the function w(x) over the distance x:
As you can see from the above equation that the magnitude of FR equal the area under the curve w(x)

## Slide 4
Statics
Distributed Loads
Location of resultant force
The location of the resultant force (d) can be found using the principle of centroid (will be discussed later) as:
x
FR
w
w = w(x)
For this stage, the location of the centroid for the given shape will be given

## Slide 5
Statics
Distributed Loads
Analysis procedures
To analyze the distributed forces you have to follow the following procedures:
  distributed load is defined as function w = w(x) with unit of N/m or lbf/ft.
  The effect of distributed load is simplified by single concentrated force acts at certain point in the body
  The resultant force equals the area under the loading diagram and acts on the centroid of this area

## Slide 6
Statics
Distributed Loads
Example 1:
x
w
200 N/m
2m
(a)
x
w
200 N/m
3m
(b)
Determine the magnitude and the location of the equivalent resultant force acting on the beam shown in the figures.

## Slide 7
Statics
Distributed Loads
Example 1:
x
w
200 N/m
2m
Solution: part a
FR = area under the loading diagram
FR = (200 N/m) (2m) = 400 N
(x’) at the center of load rectangle
x‘ = 1m
x
w
1m
400 N
You can note that the centroid of a rectangular area is its geometric center

## Slide 8
Statics
Distributed Loads
Example 1:
Solution: part b
Similar to part a
FR = area under the loading diagram
FR = (1/2)(200 N/m) (3m) = 300 N
(x’) at the centroid of triangle load
x‘ = (2/3)(3) = 2m
You can note that the centroid of a triangular area is located at a distance equal 1/3 of its height fro its base.
x
w
200 N/m
3m
x
w
2m
300 N

## Slide 9
Statics
Distributed Loads
Example 2:
Determine the magnitude and the location of the equivalent resultant force acting on the beam shown in the figure.
x
w
250 N/m
w = (30)x2 N/m
2.5m

## Slide 10
Statics
Distributed Loads
Example 2:
Solution: magnitude
x
w
156.25 N
x
w
250 N/m
w = (30)x2 N/m
2.5m
Try to solve it by your self and verify the solution

## Slide 11
Statics
Distributed Loads
Example 2:
Solution: location
x
w
156.25 N
1.875 m
x
w
250 N/m
w = (30)x2 N/m
2.5m
Try to solve it by your self and verify the solution

## Slide 12
Statics
Distributed Loads
Summary
Distributed forces are forces acting on a line or surface of the body
To deal with this kind of force, we need to represent it a single force.
The resultant force equals the area under the loading diagram and acts on the centroid of this area.

## Slide 13
Statics
Distributed Loads
End of lecture
See you in the next lecture
Don’t forget to answer the quiz