## Slide 1
Chapter Four
Laith Batarseh
Statics
4.1. condition for equilibrium +FBD
By
Home
Next
Previous
End

## Slide 2
Statics
condition for equilibrium +FBD
In this lecture
  Introduce the conditions for rigid body equilibrium
Home
Next
Previous
End
  Learn how to draw FBD (reactions analysis)

## Slide 3
Statics
condition for equilibrium +FBD
Internal, external forces and F.B.D
Internal forces are the forces caused by the interaction between body particles
Home
Next
Previous
End
External forces are the forces act on the outer surface of the body
Free – body diagram (F.B.D) shows only the external forces
Internal forces are opposite forces cancel each other

## Slide 4
Statics
condition for equilibrium +FBD
Home
Next
Previous
End
Equilibrium conditions
O
F1
F2
F3
M1
M2
Can be represented as
O
FR=0
(MR )o=0
FR = ∑F = 0 and (MR)o = ∑ Mo = 0
Assume that we have a body subjected to forces and moments system shown

## Slide 5
Statics
condition for equilibrium +FBD
Home
Next
Previous
End
Equilibrium conditions
FR = ∑F = 0 and (MR)o = ∑ Mo = 0
These equations are sufficient for any position in the body
O
FR=0
(MR )o=0
A
r
MA = r x FR + MR,O = 0
Fixed, ≠ 0
Must = 0
Assume that we have a body subjected to resultant force and moment system shown

## Slide 6
Statics
condition for equilibrium +FBD
Home
Next
Previous
End
F.B.D
To apply the equilibrium conditions successfully, all the external forces acting on the body must be specified
Free body diagram is a way to represent these forces graphically.
F.B.D is a sketch of the outlined shape of the body isolated from its surrounding (i.e. connections)
All the forces and couple moments generated from the surrounding on the body must be drawn in the F.B.D.

## Slide 7
Statics
condition for equilibrium +FBD
Home
Next
Previous
End
Support reactions
Reaction is a resistance force developed in the supporting points due to the application of external load (force)
The type of reaction in support depends on the type of motion prevented by the support.
Prevent translational motion
Reaction force
Prevent rotational motion
Reaction moment

## Slide 8
Statics
condition for equilibrium +FBD
Examples
F
F
OR
Fy
Fx
Fy
Fx
M
Roller connection
Pin connection
Cantilever connection
For more connection reactions, refer to Engineering Mechanics, Statics, 12th edition, R. C. Hibbeler, 2010, pp 202-203

## Slide 9
Statics
condition for equilibrium +FBD
Home
Next
Previous
End
Example [1]
Fy
Fx
M
2000 N
8m
Draw the F.B.D for the body shown in the figure
Solution

## Slide 10
Statics
condition for equilibrium +FBD
Home
Next
Previous
End
Example [2]
Draw the F.B.D for the body shown in the figure and find the reactions that make this system under equilibrium
100 N
200N
300 N

## Slide 11
Statics
condition for equilibrium +FBD
Home
Next
Previous
End
Example [2]
Solution
F.B.D
100 N
200N
300 N
Ry
Rx
The direction of the reactions are assumed and it will be verified later
This type of connection produces two rectangular reactions

## Slide 12
Statics
condition for equilibrium +FBD
Example [2]
Solution
Equilibrium conditions
As you see, the assumed directions are correct. In other cases where the sign associated with the reaction is opposite to the assumed direction then, the assumed direction must be reversed
Fx = 0; 100 + 200 – Rx = 0. so, Rx = -300 N
Fy = 0; -300 + Ry = 0. so, Ry = 300 N

## Slide 13
Statics
condition for equilibrium +FBD
Summary
Free body diagram is a graphical method used to represent the forces that act on a body
To draw F.B.D, you must separate the body from its surrounding and draw the forces.
There is resistance to motion produced in the connections that connect the body with other bodies or the surrounding. This resistance is called reaction.
The type of generated reactions in connections depends on the type of the connection

## Slide 14
Statics
condition for equilibrium +FBD
Summary
In general, the reactions developed in connection may be a force and/or moment
When the connection restrict the body from a translational motion in one direction then a reaction force is generated in the connection in the opposite direction
When the connection restrict the body from a rotational motion in one direction then a reaction moment is generated in the connection in the opposite direction

## Slide 15
Statics
condition for equilibrium +FBD
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz