## Slide 1
Chapter Four
Laith Batarseh
Statics
4.2. equations of equilibrium
By
Home
Next
Previous
End

## Slide 2
Statics
Equations of equilibrium
In this lecture
  Learn how to use equilibrium equations to find unknown reactions or forces
Home
Next
Previous
End

## Slide 3
Statics
Equations of equilibrium
Equations of equilibrium
as said previously, the body will be under equilibrium if the summation of both resultant forces and moments equal zero
Home
Next
Previous
End
Mathematically, ∑F = ∑M = 0
In planer forces (2D problems), the rectangular notation for forces is very useful
∑Fx = 0
∑Fy = 0
∑Mo = 0

## Slide 4
Statics
Equations of equilibrium
Alternative set of equilibrium equations
In some cases we can use only the equilibrium of forces equations or the moment equation only
Home
Next
Previous
End
The main criteria that determine the number of equations used to solve a problem is the number of the unknowns
Algebraically, to solve a certain number of unknowns, you need the same number of equations. For example, you can solve 4 equations with 4 unknowns

## Slide 5
Statics
Equations of equilibrium
Analysis procedures
Establish F.B.D with all the acting forces and couple moments beside the reaction forces and moments shown clearly.
Home
Next
Previous
End
Use the equilibrium equations to find the unknown reactions, forces or moments required. These equations are ∑Fx = ∑Fy = ∑M = 0
If the assumed force or moment show an opposite sense (i.e. different sign from the originally assumed) the sense of force or moment must be reversed
It is preferred to use equilibrium moment equation at the reaction that have two unknowns to eliminate them

## Slide 6
Statics
Equations of equilibrium
Example [1]
Draw the F.B.D for the body shown in Fig. 1 and find the reactions at both points A and B that make this system under equilibrium
Home
Next
Previous
End
250 N
500 N
400 N
30o
2m
1.5m
3.5 m
A
B
Fig.1

## Slide 7
Statics
Equations of equilibrium
Example [1]
Solution
Home
Next
Previous
End
F.B.D
250 N
500 sin(30)N
400 N
2m
1.5m
3.5 m
Ax
Ay
By
500 cos(30)N

## Slide 8
Statics
Equations of equilibrium
Example [1]
Solution
Home
Next
Previous
End
Equilibrium equations
Back to Eq.1

## Slide 9
Statics
Equations of equilibrium
Example [2]
Draw the F.B.D for the body shown in Fig.2 and find the reactions at the supporting points that make this system under equilibrium
Home
Next
Previous
End
9 kN
w(x) = x2 kN/m
3m
3m
A
C
x
y
B
Fig.2

## Slide 10
Statics
Equations of equilibrium
Example[2]
Solution
Home
Next
Previous
End
First, We divide the distributed load w(x) into two identical regions: A→B and B→C. then, we must find the resultant force FR for each region. By using the method of reduction distrusted loads that we learn previously, FR can be found for region A→B as:
the location of FR (x’) is found as:

## Slide 11
Statics
Equations of equilibrium
Example[2]
Solution
Home
Next
Previous
End
Due to the symmetry between the two regions (A→B and B→C), the reduction process of the distributed load acting on region A→B can be ,simply, duplicated to find the magnitude and the location of the resultant force acting on region B→C. now we can represent these forces on the beam:
9 kN
3m
3m
A
C
B
2.25 m
2.25 m
9 kN

## Slide 12
Statics
Equations of equilibrium
Example[2]
Solution
Home
Next
Previous
End
After reducing the distributed loads, the time now is appropriate to draw F.B.D. The F.B.D is shown in Fig.3
9 kN
A
C
4.5 m
Fig.3
0.75m
0.75m
9 kN
Ax
Ay
Cy
Again the direction of the reaction were assumed randomly.

## Slide 13
Statics
Equations of equilibrium
Example[2]
Solution
Home
Next
Previous
End
As you can see, there is no force acting on this body at x-direction. So, Ax = 0 and the summation of forces at y-direction yield to:
By + Ay = 9+9 = 18 kN ---- (1)
applying the equilibrium equation about a certain point for example point A to find the reaction By:
∑MA = 0 → (9)(4.50+0.75)+(9)(0.75) – By (6) --- (2)
Rearrange Eq.2 and solve for By: By = 9kN↑ Ans
. Back to Eq.2, substitute the value of By to find Ay:
Ay + 9 = 18 → Ay = 9N Ans

## Slide 14
Statics
Equations of equilibrium
Example[2]
Solution
Home
Next
Previous
End
You can note:
Because of the symmetry in this problem, the reactions were identical. Such note can be generalized on other symmetrical system.
You can use the momentum equation again to find Ay instead of using the force equation. This procedure can be used also to verify the solution

## Slide 15
Statics
Equations of equilibrium
Home
Next
Previous
End
We reached the end of lecture
See you in the next lecture
Don’t forget to answer the quiz