## Slide 1
Chapter Five
Laith Batarseh
Statics
5.2 Method of joints
By
Home
Next
Previous
End

## Slide 2
Statics
Method of joints
In this lecture we will
Home
Next
Previous
End
  Introduce the main principle of method of joint
  Lean how this method satisfy the equilibrium conditions
  Lean how to use this method to find the member force

## Slide 3
Statics
Method of joints
Method of joints
Is a method used to find the forces acting inside a truss member
It is based on the fact that the member is entirely under equilibrium and therefore each joint is also under equilibrium
since the trusses are planar, the member can be assumed to be two forces member.
This method depends directly on applying the equation of force equilibrium (∑Fx= 0 and ∑Fy = 0) at the joints.
We first start with assuming the member force as unknown and then use the equilibrium equations to find it then move to the 2nd joint in the member, which is connected to other member(s) to find other members unknowns.
This method is consecutive method. You start from a one joint and continuo to solve for the rest of joints.

## Slide 4
Statics
Method of joints
Force directions
When assuming the unknown forces, the direction of the force can be assumed by one of the following:
  the sense of member force is assumed by common sense: if it try to pull the joint it will be tension and if it try to push the joint it will be a compression. This can be done, also, by satisfying the equations of equilibrium on the joint as shown in the figure. As you can see, the 100N force acts on the joint where there are two unknown member forces (F1 and F2) also act on the same joint.
100 N
F1
F2
??
??

## Slide 5
Statics
Method of joints
Force directions
To assume that this joint under equilibrium, the force F2 must has a sense as shown in figure (a) to insure that there is a component neutralize the 100N force. With this result, we still have to find the sense of force F1. as shown in figure (b), there is a vertical component generated from the assumption of force F2 direction This implies that the sense of the force F1 must be in a way to neutralize this component as shown in figure (b). Figure (c) show the final sense of members forces
100 N
F1
F2
??
F2,x
F2,y
(a)
100 N
F1
F2
F2,x
F2,y
(b)
100 N
F1
F2
(c)

## Slide 6
Statics
Method of joints
Force directions
  the 2nd method to assume the sense of members forces is to assume all the member forces are tension which are represented in a positive scalar quantity. Now, if the numerical calculations yield a force with a negative sign (negative scalar quantity), then this force is a compression and its sense must be reversed.
  Now, both methods may be used. However, it may be preferred to use the first one because it reduce the verification step and it is more convenient when dealing with large truss configurations.

## Slide 7
Statics
Method of joints
Equations of equilibrium
  As mentioned before, we have two equilibrium equations:
Because truss member is a two force member and a planar forces, the forces acting on a joint are coplanar and concurrent. Therefore, the equation of moment equilibrium gives a trivial solution.
There is an important note must be mentioned: because we have two equilibrium equations, we can solve for two unknowns only. So, to apply the method of joints, the joint under analysis must have, maximum, 2 unknowns.
∑Fx = 0
∑Fy = 0

## Slide 8
Statics
Method of joints
Analysis procedures
  To use the method of joints, you can follow these procedures:
  Choose a joint that has a two unknowns and draw F.B.D for that joint.
  Use one of the two methods descried previously to assign the direction of unknown forces.
  Establish the x-y coordinate system and be sure that the origin of the coordinate system is at the joint.
  Resolve the unknown forces to their rectangular components
  Use equilibrium equations: ∑Fx = 0 and ∑Fy = 0 to find the unknown rectangular components.
  Repeat the previous procedures to analyze the rest of joints and find all the unknowns

## Slide 9
Statics
Method of joints
Example [1]
Determine the force in each member of the truss shown in the figure
100 N
60O
60O
2m
A
B
C

## Slide 10
Statics
Method of joints
Example [1]
Solution
Let us choose joint B as a start point because it has three forces: 100N, FAB and FBC. As you can notice, this joint is subjected to two unknowns: FAB and FBC. Figure (a) shows F.B.D for joint B:
Now, let us resolve the unknown forces to their rectangular components as shown in figure (b)
B
FAB,y
FBC,x
(b)
x
y
FAB,x
100 N
FBC,y
B
FAB
FBC
(a)
x
y
100 N
60O
60O

## Slide 11
Statics
Method of joints
Example [1]
Solution
Now, apply the equilibrium equations
∑Fx = 0 → -FABcos(60)-FBCcos(60) +100 = 0 ---- (1)
∑Fy = 0 → -FABsin(60)+FBCsin(60) = 0 →FAB = FBC
Note the how the symmetry in the shape is reflected on the magnitude of forces
Back now to Eq(1)
-2FABcos(60) +100 = 0 → FAB = 100 N = FBC

## Slide 12
Statics
Method of joints
Example [1]
Solution
Let us now go to joint C because it has two unknowns: FAC and FBC. Figure (a) shows F.B.D for joint C.
As in the previous joint, let us resolve the unknown forces to their rectangular components as shown in figure (b)
C
FAC
FBC = 100N
(a)
x
y
Cy
60O
B
(b)
x
y
FAC
100 cos(60)
100 sin(60)
Cy

## Slide 13
Statics
Method of joints
Example [1]
Solution
Now, apply the equilibrium equations
∑Fx = 0 → 100 cos(60) – FAC = 0 → FAC = 50 N
∑Fy = 0 → Cy – 100sin(60)= 0 →Cy = 86.6 N
At this point, we find the forces inside the members. Now, try by your to find the reactions at the support A.
A
x
y
Ax
Ay
FAC
FAB
60O

## Slide 14
Statics
Method of joints
Home
Next
Previous
End
We reached the end of this lecture
Please don’t forget to answer the quiz
See you in the next one