## Slide 1
Chapter Five
Laith Batarseh
Statics
5.2 Method of joints – part II
By
Home
Next
Previous
End

## Slide 2
Statics
Method of joints
In this lecture we will
Home
Next
Previous
End
  Introduce the concept of zero force members
  Recognize the zero-force member in truss configuration
  Illustrate their effects on the equilibrium conditions

## Slide 3
Statics
Method of joints
Zero forces members
Zero force member is a member that experience no force inside it.
Such members are used to give the structure more stability
in the calculations of the unknowns using equilibrium conditions, these members create a state of statically in-determent because it add a new unknowns to the problem. However, if you analyze a joint that have more than two unknowns, you must ask your self: are there a zero-force members connected to this joint. Because if there was zero force member, the force inside this member is out of the equilibrium equations.
The best way to find a zero-force member is by inspection

## Slide 4
Statics
Method of joints
Example on zero forces members
See the figure below which illustrates a truss and the F.B.D for selected joints: D and C. as you can see, the force in member ED (FED) cancel the force in the member DC (FDC) and so, the Force in member AD (FAD) must equal zero to achieve equilibrium conditions
A
B
C
D
E
F
FED
FAD
FAC
FDC
FCB
Similar conclusion can be said about the member connected at joint C. this means that FAC is also equal zero.
Members AD and AC are called zero force members and the system will be stable and under equilibrium without them

## Slide 5
Statics
Method of joints
Example on zero forces members
You can conclude also that the joint which has a three members where two of the members have a collinear forces then the third member will be a zero-force member.
A
B
C
D
E
F
FED
FAD
FAC
FDC
FCB
So, in general, we must first examine the truss configuration to find the zero forces members and eliminate these members from the equilibrium calculations.

## Slide 6
Statics
Method of joints
Example [1]
Determine the zero-force members in the truss shown in the figure.
A
B
C
D
E
F
G
H
F1
F2

## Slide 7
Statics
Method of joints
Example [1]
Solution
To find the zero-forces members, we must search for the three or more forces joints. These joints are: B, C, D, F, G and H.
A
B
C
D
E
F
G
H
F1
F2
FBC
FBA
FBH
Now we must search for the joints that have two collinear forces which are: B, G and H. let us start with joint B. as you can see, the forces in members BA and BC cancel each
other and so the Force in member BH
(FBH) must equal zero to maintain
equilibrium

## Slide 8
Statics
Method of joints
Example [1]
Solution
Now let us take joint G. as you can see, the forces in members HG and GF cancel each other and so the Force in member CG (FCG) must equal zero to maintain equilibrium.
Finally the analysis of joint H. this joint has 4 members. However, we find that the force FBH
equal zero and from the F.B.D, force FAH cancel
the force FHG which means that the member
CH is a zero-force member.
A
B
C
D
E
F
G
H
F1
F2
FBH
FHG
FGF
FCG
FAH
FCH

## Slide 9
Statics
Method of joints
Summary
The method of joints is based on the fact that the member is entirely under equilibrium and therefore each joint is also under equilibrium
The unknowns are found by applying the equation of force equilibrium (∑Fx= 0 and ∑Fy = 0) at the joints
The sense (direction) of the unknown forces are assumed at the beginning of solving process and then it may be verified
This method starts with a joint has two unknown only then move forward to the other joints. And so, the joints that have more than two unknowns are left to last

## Slide 10
Statics
Method of joints
Summary
In trusses, we may face the zero force member
Zero force member is a member does not subjected to internal load.
Zero force member is used to increase the stability of the truss and it create statically in-determent issue if it is not being out of equilibrium calculations
the joint which has a three members where two of the members have a collinear forces then the third member will be a zero-force member.

## Slide 11
Statics
Method of joints
Home
Next
Previous
End
We reached the end of this lecture
Please don’t forget to answer the quiz
See you in the next one