## Slide 1
Chapter Five
Laith Batarseh
Statics
5.3 method of sections
By
Home
Next
Previous
End

## Slide 2
Statics
Method of sections
In this lecture we will
  Introduce the concept of method of sections
Home
Next
Previous
End
  Use this method to solve truss problems

## Slide 3
Statics
Method of sections
Method of sections
Is a method used mainly to find member forces in few number of members.
it is based on the fact that if a truss is under equilibrium, then any segment in the truss is also under equilibrium. To illustrate this principle, see the figure below.
The plane used to cut the member is called section
Compression
Tension

## Slide 4
Statics
Method of sections
Analysis procedures
Drawing F.B.D
First, chose appropriate section which isolate the members that you with to find there unknown forces
In most cases, we need to find the reactions at the supporting points before isolating the chosen section. This can be done easily by using equilibrium equations.
Draw F.B.D for the chopped section
Define the direction of forces using one of the methods discussed in the method of joints: by inspection or by assuming all the forces are tension and then verify this assumption using the numerical calculation

## Slide 5
Statics
Method of sections
Analysis procedures
Equilibrium equations
We must be carful when select the appropriate equilibrium equation to find the unknowns. As you remember, applying the moment equation at intersecting point of lines of action for two forces eliminate them and so we can find a third unknown force. So, you may start with applying the moment equation at a common intersecting point of forces lines of actions.
In some cases we can use the principle of transmissibility and slide a force to a certain point and then resolve it into its rectangular components. This procedure insure, in many situations, eliminating one of the unknown force components. the principle of transmissibility implies that we can move the force along its line of action.

## Slide 6
Statics
Method of sections
Examples [1]
Determine the force in members FE, FC, and BC of the truss shown in the figure
4m
4m
4m
3m
1000 N
500 N
A
B
C
D
E
F

## Slide 7
Statics
Method of sections
Examples [1]
Solution
We can start with finding the reactions at connections A and D. the figure below shows the F.B.D for the whole truss
Now, we apply equilibrium equations to find the supports reactions:
∑Fx= 0 → 500 – Ax = 0 → Ax = 500N
∑MA= 0 → -1000(8) – 500(3) + Dy(12) = 0 → Dy = 792N
∑Fy = 0 → Ay – 1000 +792 = 0 → Ay = 208 N
4m
4m
4m
3m
1000 N
500 N
A
B
C
D
E
F
Ax
Ay
Dy

## Slide 8
Statics
Method of sections
Examples [1]
Solution
Now let us make a section s-s as shown in figure below
500 N
208 N

## Slide 9
500 N
208 N
Statics
Method of sections
Examples [1]
Solution
We can apply equilibrium equations to find the unknown member forces:
Summation of moments at point F:
∑MF= 0 → FBC(3) – 208(4) – 500(3)= 0 → FBC= 777N
Summation of moments at point C:
∑MC= 0 → FFE(3) – 208(4) = 0 → FFE= 277N
Summation of forces in y-direction:
∑Fy = 0 → 208 – FFC(3/5) = 0 → FFC = 357N

## Slide 10
Statics
Method of sections
Examples [2]
Determine the force in member EB of the truss shown in the figure
500 N
1000 N
500 N
A
2000 N
1500 N
B
C
D
E
F
500 N
2m
2m
2m
2m
30o
30o
30o
30o

## Slide 11
Statics
Method of sections
Examples [2]
Solution
As you can see, joint (E) connect four members and joint (B) connect five members. So, it may be more convenient to section this truss from joint (E) although this joint create statically in-determent situation due to the presence of three unknown forces.
To overcome this problem, we can make two sections, one to find one of the unknowns and the other to satisfy the requirement of this problem which is finding FEB.

## Slide 12
Statics
Method of sections
Examples [2]
Solution
The two chosen sections are shown in figure below. As you can see, the section b-b can be used to find FEB if one of the other unknown forces is found. Our strategy is to find FEC from section a-a and then go back to section b-b and with the aid of equilibrium conditions, we can find our requirement.
a
a
FEC
FEB
FBF
FAB
b
b
FED
FEF
FEB

## Slide 13
a
a
FEC,x
FEC
FEC,y
FEB
FBF
FAB
Statics
Method of sections
Examples [2]
Solution
To find FEC, we use the principle of transmissibility and slide this force to point C as shown. Then we can resolve it to its components. Apply the moment equation at point (B):
∑MB= 0 →-500(4) – 1500(2) + 2000(4) – FEC sin(30)(4)= 0
→ FEC= 1500 N

## Slide 14
Statics
Method of sections
Examples [2]
Solution
After finding FED, we now can take the section b-b and apply the force equilibrium equations at this point:
Summation of forces in x-direction:
∑Fx = 0 → FEF cos(30) – 1500 cos(30) = 0 → FEF = 1500N
Summation of forces in y-direction:
∑Fy = 0 → 1500 sin(30) + 1500 sin(30) – 500 - FEB= 0
→ FEB = 1000N
b
b
1500
FEF
FEB

## Slide 15
Statics
Method of sections
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz