## Slide 1
Chapter seven
Laith Batarseh
Statics
7.1. Dry friction
By
Home
Next
Previous
End

## Slide 2
Statics
Dry friction
In this lecture we will
  Define the dry friction concept
  Introduce the characteristics of dry friction
  Introduce the theory of dry friction

## Slide 3
Statics
Dry friction
Dry friction
  Friction is a resistance for motion between two contacting surfaces.
  The term Dry Friction is giving to the friction force if there is no lubricating fluid between the surfaces.
  Some times the dray friction is called Coulomb friction referred to scientist Coulomb (1781).

## Slide 4
Statics
Dry friction
Dry friction
F
w
F
w
Friction force,Fs
Normal force, N
Resistance force
CG

## Slide 5
Statics
Dry friction
Dry friction
Equilibrium conditions
F
w
Fs
N
h
x

## Slide 6
Statics
Dry friction
Impeding monition
If we increase the applied force F slowly, then the value of the friction Fs will increase in the same value to hold the system under equilibrium.
However, if we continuo increasing the applied load we will reach a point where the friction reach its maximum value. This value is called limiting static frictional force, Fmax.
At this value, the system will be unstable equilibrium situation because any increasing in the applied load will cause a motion in the system.

## Slide 7
Statics
Dry friction
Impeding monition
It was found experimentally that the value of the static friction force, Fs is proportionally related to the normal force, N which is equal to the weight of the body .
Mathematically, maximum friction and normal forces are related by:
Fmax = μs N
Where: μs is the coefficient of static friction.
The value of μs depends on the type of contacting material surface roughness and area.

## Slide 8
Statics
Dry friction
Motion with friction
When the value of the applied load exceed the limiting static frictional force, the system will move (slide) under the effect of the difference between the applied load and the friction.
in spite of the motion, the friction will remain in the system. Because of the kinetic behavior of the body, the friction is called kinetic friction, Fk
The experiments done on kinetic friction show that the value of kinetic friction, Fk is proportionally related to the normal force, N by the following relation:
Fk= μk N
Where: μk is the coefficient of kinetic friction.

## Slide 9
Statics
Dry friction
Motion with friction
In general, the behavior of the friction developed between the contact surfaces is shown in the following graph:
Fmax
Fk
Fs=F
45o
Fs
F

## Slide 10
Statics
Dry friction
Characteristic of dry friction
It is tangent to the contacting surfaces in a direction opposite to the applied load.
The value of maximum friction force depends on the pressure produced by the normal force which means it depends on: the value of the normal force and the contacting area between the surfaces.
Before the slipping (motion), the friction is called static and the body still static. When the value of the applied load exceed the maximum friction force, the body will be in motion and the friction will remain constant and is called kinetic friction.
The relation between the friction and normal force is proportional and the proportionality constants are: μs and μk.

## Slide 11
Statics
Dry friction
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz