## Slide 1
Chapter seven
Laith Batarseh
Statics
By
Home
Next
Previous
End
7.2. Friction in screws and belts

## Slide 2
Statics
Friction in Screws and Belts
In this lecture we will
  Determine the formula of friction in screws
  Determine the formula of friction in belt – pulley configuration.

## Slide 3
Statics
Friction in Screws and Belts
Screws
  Screws are threaded cylindrical peaces of metals and used as fasteners (to join parts) or to transmit power (power screws).
  In the case of power screw, the shape of thread is mainly square as the one shown below.

## Slide 4
Statics
Friction in Screws and Belts
Screws
  the motion of screw is done by a moment (M):
  M = r W tan(фs+Ө)
  Where:
  W is the vertical force acting on thread
  Фs is angle of static friction = tan-1(F/N) = tan-1(μs)
  Ө = tan-1(l/2πr)
r
l
l
2πr
Ө

## Slide 5
Statics
Friction in Screws and Belts
Belts
T1
T2
T2
T1
β

## Slide 6
Statics
Friction in Screws and Belts
Example [1] 8-77
The square threaded screw of the clamp has a mean diameter of 14 mm and a lead of 6 mm. If μs= 0.2 for the threads, and the torque applied to the handle is 1.5 N . m, determine the compressive force F on the block

## Slide 7
Statics
Friction in Screws and Belts
Example [1] 8-77
Solution
The angle Ө is found as:
  Ө = tan-1(l/2πr) = tan-1(6/2π(7)) = 7.8o
  W = F and фs =tan-1(μs) = 11.3o.
  Apply M = r W tan(фs+Ө) → 1.5 = F(0.007) tan(7.8+11.3)
  → F = 620 N

## Slide 8
Statics
Friction in Screws and Belts
Example [1] 8-107
The drive pulley B in a video tape recorder is on the verge of slipping when it is subjected to a torque of M = 0.005 N.m . If the coefficient of static friction between the tape and the drive wheel and between the tape and the fixed shafts A and C is μs= 0.1 , determine the tensions T1and T2 developed in the tape for equilibrium.

## Slide 9
Statics
Friction in Screws and Belts
Example [1] 8-77
Solution
F.B.D

## Slide 10
Statics
Friction in Screws and Belts
Example [1] 8-77
Solution
T3 must overcome T4 and M. So T3>T4
From F.B.D and the equilibrium equations
Solve Eqs 1and 2 to find T3 and T4:
T3 = 1.85N and T4 = 1.35N
Back to shaft A and C to find T1 and T2:

## Slide 11
Statics
Friction in Screws and Belts
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz