## Slide 1
Chapter eight
Laith Batarseh
Statics
8.4. resultant of distributed Loads-I
By
Home
Next
Previous
End

## Slide 2
Statics
resultant of distributed Loads
Definition
x
w
L
w = w(x)
x
w
L
dF = dA
x
dx
w = w(x)
Magnitude of resultant force
Location of resultant force
The centroid

## Slide 3
Statics
resultant of distributed Loads
Example[1]: problem 9-105
The concrete “gravity” dam is held in place by its own weight. If the density of concrete is 2.5 Mg/m3, and water has a density of 1 Mg/m3 , determine the smallest dimension d that will prevent the dam from overturning about its end A

## Slide 4
Statics
resultant of distributed Loads
Example[1]: problem 9-105
Solution
F.B.D
F

## Slide 5
Statics
resultant of distributed Loads
Example[1]: problem 9-105
Solution
The pressure produced by the water depends on the depth and is related by:
P = ρ g h
Where :
ρ is water density
g is the gravitational acceleration
h is the depth
And so, the pressure will has a maximum value at the base of the dam where h=6m and zero at the surface . Mathematically:
P6m = (1000)(9.81)(6) =58860 N/m

## Slide 6
Statics
resultant of distributed Loads
Example[1]: problem 9-105
Solution
Now, let us relate the distributed pressure to force (Fdis):
Fdis = P*Area
Let the width of the dam equal 1m to have a unity area. So,
Fdis = P
Finally, the distributed load is reduced to a single force act at the centroid of loading area:
F = (0.5)(5886)(6) = 176580 N
Then, we can Find that the weight of the dam (w) can be found as:
W= (0.5)(d)(6)(1)(2500)(9.81) = 73575d

## Slide 7
Statics
resultant of distributed Loads
Example[1]: problem 9-105
Solution
Apply the moment equilibrium equation at point A :
176580(2) = 73575 (2/3)d
d = 2.68 m (for each 1m depth of the dam)

## Slide 8
Statics
resultant of distributed Loads
Example[2]: problem 9-106
The symmetric concrete “gravity” dam is held in place by its own weight. If the density of concrete is 2.5 Mg/m3, and water has a density of 1 Mg/m3 , determine the smallest dimension d that will prevent the dam from overturning about its end A. The dam has a width of 8 m

## Slide 9
Statics
resultant of distributed Loads
Example[2]: problem 9-106
Solution
F.B.D
As you can see, the area (1) act as a weight at the dam surface and the area (2) apply a pressure at the same surface.

## Slide 10
Statics
resultant of distributed Loads
Example[2]: problem 9-106
Solution
Area (1)
Area (2)
Dam weight (W)

## Slide 11
Statics
resultant of distributed Loads
Example[2]: problem 9-106
Solution
Moment equation

## Slide 12
Statics
resultant of distributed Loads
Home
Next
Previous
End
End of lecture
See you in the next lecture
Don’t forget to answer the quiz